## Slide 1
CPR E 281: Digital Logic
Md Maruf Ahamed Office: 307 Durham Center Phone: (515) 294-6323 Email: maruf@iastate.edu

## Slide 2: Administrative Stuff
  Homework: HW#4 due on Sunday @ 11:59 PM
  Quiz: Quiz #4 due on Friday @ 4:25 PM
  Recitation: Recitation #05 this week
  Lab: Lab # 05 this week
      Submit pre-lab prior to the lab otherwise you will lose 20% points
  Lecture-16 Readings: Section 3.6
  Mini Project next week
    Submit pre-lab prior to the lab otherwise you will lose 20% points

## Slide 3: 15–Fast Adders
  Fast Adders
  How to build Fast Adder circuits
  Carry-Lookahead Adder
  Hierarchical CLA Adder Carry Logic

## Slide 4
b
n
1
–
b
1
b
0
Magnitude
MSB
(a) Unsigned number
b
n
1
–
b
1
b
0
Magnitude
Sign
(b) Signed number
b
n
2
–
0 denotes
1 denotes
+
–
MSB
Formats for representation of integers
[ Figure 3.7 from the textbook ]
Sign and magnitude
1’s complement
2’s complement
Negative numbers can be represented in following ways:

## Slide 5
Find the 1’s complement of …
0 1 0 1
0 0 1 0
0 1 1 1
0 0 1 1
1 0 1 0
1 1 0 1
1 0 0 0
1 1 0 0
Just flip 1's to 0's and vice versa.

## Slide 6
Example of 1’s complement addition
[ Figure 3.8 from the textbook ]
But this is +2!

## Slide 7
Find the 2’s complement of …
0 1 0 1
0 0 1 0
0 1 1 1
0 1 0 0
1 0 1 0
1
1 0 1 1
+
1 0 1 1
1
1 1 0 0
+
1 0 0 0
1
1 0 0 1
+
1 1 0 1
1
1 1 1 0
+
Then add 1.

## Slide 8: Quick Way to find 2’s complement
Scan the binary number from right to left
Copy all bits that are 0 from right to left
Stop at the first 1
Copy that 1 as well
Invert all remaining bits
0 1 1 0

## Slide 9
Example of 2’s complement addition
[ Figure 3.9 from the textbook ]

## Slide 10
s
0
s
1
s
n
1
–
x
0
x
1
x
n
1
–
c
n
n
-bit adder
y
0
y
1
y
n
1
–
c
0
Add
¤
Sub
control
[ Figure 3.12 from the textbook ]
Adder/subtractor unit

## Slide 11
+
+
1 0 1 1
1 0 0 1
0 0 1 0
1 0 0 1
0 1 1 1
0 0 1 0
7
+
(
)
2
+
(
)
9
+
(
)
+
+
+
0 1 1 1
1 0 0 1
1 1 1 0
0 1 0 1
0 1 1 1
1 1 1 0
7
+
(
)
5
+
(
)
+
2
–
(
)
1
1
2
+
(
)
7
–
(
)
5
–
(
)
+
7
–
(
)
9
–
(
)
+
2
–
(
)
Examples of determination of overflow
0 1 1 0 0
0 0 0 0 0
1 0 0 0 0
1 1 1 0 0
c
4
0
=
c
3
1
=
c
4
1
=
c
3
1
=
c
4
0
=
c
3
0
=
c
4
1
=
c
3
0
=
Overflow = c3c4 + c3c4
XOR

## Slide 12
FA
x
n –
1
c
n
c
n
1
y
n
1
–
s
n
1
–
FA
x
1
c
2
y
1
s
1
FA
c
1
x
0
y
0
s
0
c
0
Detecting Overflow
(with one extra XOR)
overflow
-

## Slide 13
X= x3 x2 x1 x0
Y= y3 y2 y1 y0
S= s3 s2 s1 s0
+
Another way to look at the overflow issue

## Slide 14
+
+
1 0 1 1
1 0 0 1
0 0 1 0
1 0 0 1
0 1 1 1
0 0 1 0
7
+
(
)
2
+
(
)
9
+
(
)
+
+
+
0 1 1 1
1 0 0 1
1 1 1 0
0 1 0 1
0 1 1 1
1 1 1 0
7
+
(
)
5
+
(
)
+
2
–
(
)
1
1
2
+
(
)
7
–
(
)
5
–
(
)
+
7
–
(
)
9
–
(
)
+
2
–
(
)
Examples of determination of overflow
x
3
0
=
y
3
0
=
s
3
1
=
x
3
0
=
y
3
1
=
s
3
0
=
x
3
1
=
y
3
0
=
s
3
1
=
x
3
1
=
y
3
1
=
s
3
0
=
Overflow = x3 y3 s3 + x3 y3 s3

## Slide 15
X= x3 x2 x1 x0
Y= y3 y2 y1 y0
S= s3 s2 s1 s0
+
Another way to look at the overflow issue
If both numbers that we are adding have the same sign
but the sum does not, then we have an overflow.
Overflow = x3 y3 s3 + x3 y3 s3

## Slide 16: Practice Problem 2
Perform the following operations in 2's complement form and identify, if there is any overflow occurs or not.
    (-1310)
    + (- 410)
    -------------------------------------

## Slide 17
Fast Adders
Readings 3.4, 3.5

## Slide 18: Can we perform addition even faster?
The goal is to evaluate very fast if the carry from the previous stage will be equal to 0 or 1.

## Slide 19
The Full-Adder Circuit
[ Figure 3.3c from the textbook ]
Let's take a closer look at this.

## Slide 20
Decomposing the Carry Expression
ci+1 = xi yi + xi ci + yi ci

## Slide 21
Decomposing the Carry Expression
ci+1 = xi yi + xi ci + yi ci
ci+1 = xi yi + (xi + yi )ci

## Slide 22
Decomposing the Carry Expression
yi
xi
ci+1
ci
ci+1 = xi yi + xi ci + yi ci
ci+1 = xi yi + (xi + yi )ci

## Slide 23
Another Way to Draw the Full-Adder Circuit
yi
xi
ci
ci+1
si
ci+1 = xi yi + xi ci + yi ci
ci+1 = xi yi + (xi + yi )ci

## Slide 24
Another Way to Draw the Full-Adder Circuit
ci+1 = xi yi + (xi + yi )ci
yi
xi
ci
ci+1
si

## Slide 25
Another Way to Draw the Full-Adder Circuit
ci+1 = xi yi + (xi + yi )ci
gi
pi
yi
xi
ci
ci+1
si

## Slide 26
Another Way to Draw the Full-Adder Circuit
ci+1 = xi yi + (xi + yi )ci
gi
pi
g - generate
p - propagate
yi
xi
ci
ci+1
si
gi
pi

## Slide 27
Yet Another Way to Draw It (Just Rotate It)
ci
ci+1
si
xi
yi
pi
gi

## Slide 28
x
1
y
1
g
1
p
1
s
1
Stage 1
x
0
y
0
g
0
p
0
s
0
Stage 0
c
0
c
1
c
2
Now we can Build a Ripple-Carry Adder
[ Figure 3.14 from the textbook ]

## Slide 29
x
1
y
1
g
1
p
1
s
1
Stage 1
x
0
y
0
g
0
p
0
s
0
Stage 0
c
0
c
1
c
2
Now we can Build a Ripple-Carry Adder
[ Figure 3.14 from the textbook ]

## Slide 30
x
1
y
1
g
1
p
1
s
1
Stage 1
x
0
y
0
g
0
p
0
s
0
Stage 0
c
0
c
1
c
2
The delay is 5 gates (1+2+2)

## Slide 31
x
1
y
1
g
1
p
1
s
1
Stage 1
x
0
y
0
g
0
p
0
s
0
Stage 0
c
0
c
1
c
2
n-bit ripple-carry adder: 2n+1 gate delays
. . .

## Slide 32
Decomposing the Carry Expression
ci+1 = xi yi + xi ci + yi ci

## Slide 33
Decomposing the Carry Expression
ci+1 = xi yi + xi ci + yi ci
ci+1 = xi yi + (xi + yi )ci
gi
pi

## Slide 34
Decomposing the Carry Expression
ci+1 = xi yi + xi ci + yi ci
ci+1 = xi yi + (xi + yi )ci
gi
pi
(1 gate delay)
(1 gate delay)

## Slide 35
x
1
y
1
g
1
p
1
s
1
Stage 1
x
0
y
0
g
0
p
0
s
0
Stage 0
c
0
c
1
c
2
It takes 1 gate delay to compute all pi signals
[ Figure 3.14 from the textbook ]

## Slide 36
x
1
y
1
g
1
p
1
s
1
Stage 1
x
0
y
0
g
0
p
0
s
0
Stage 0
c
0
c
1
c
2
It takes 1 gate delay to compute all gi signals
[ Figure 3.14 from the textbook ]

## Slide 37
Decomposing the Carry Expression
ci+1 = xi yi + xi ci + yi ci
ci+1 = xi yi + (xi + yi )ci
gi
pi

## Slide 38
Decomposing the Carry Expression
ci+1 = xi yi + xi ci + yi ci
ci+1 = xi yi + (xi + yi )ci
gi
pi
ci+1 = gi + pi ci

## Slide 39
Decomposing the Carry Expression
ci+1 = xi yi + xi ci + yi ci
ci+1 = xi yi + (xi + yi )ci
gi
pi
ci+1 = gi + pi ci
ci+1 = gi + pi (gi-1 + pi-1 ci-1 )
ci
recursive
expansion of

## Slide 40
Decomposing the Carry Expression
ci+1 = xi yi + xi ci + yi ci
ci+1 = xi yi + (xi + yi )ci
gi
pi
ci+1 = gi + pi ci
ci+1 = gi + pi (gi-1 + pi-1 ci-1 )
ci+1 = gi + pi gi-1 + pi pi-1 ci-1

## Slide 41
x
1
y
1
g
1
p
1
s
1
x
0
y
0
s
0
c
2
x
0
y
0
c
0
c
1
g
0
p
0
[ Figure 3.15 from the textbook ]
Now we can Build a Carry-Lookahead Adder
c2 = g1 + p1 g0 + p1 p0 c0

## Slide 42
x
1
y
1
g
1
p
1
s
1
x
0
y
0
s
0
c
2
x
0
y
0
c
0
c
1
g
0
p
0
The first two stages of a carry-lookahead adder
[ Figure 3.15 from the textbook ]
. . .
Stage 0
Stage 1

## Slide 43
c1 = g0 + p0 c0
Carry for the first stage
ci+1 = gi + pi ci

## Slide 44
x
1
y
1
g
1
p
1
s
1
x
0
y
0
s
0
c
2
x
0
y
0
c
0
c
1
g
0
p
0
c1 = g0 + p0 c0
Carry for the first stage

## Slide 45
Carry for the second stage
c2 = g1 + p1g0 + p1p0c0
ci+1 = gi + pi gi-1 + pi pi-1 ci-1

## Slide 46
x
1
y
1
g
1
p
1
s
1
x
0
y
0
s
0
c
2
x
0
y
0
c
0
c
1
g
0
p
0
c2 = g1 + p1g0 + p1p0c0
Carry for the second stage

## Slide 47
Carry for the first two stages
c1 = g0 + p0 c0
c2 = g1 + p1g0 + p1p0c0

## Slide 48
Carry for the first two stages
c1 = g0 + p0 c0
c2 = g1 + p1g0 + p1p0c0

## Slide 49
Carry for the first two stages
c1 = g0 + p0 c0
c2 = g1 + p1g0 + p1p0c0
= g1 + p1 (g0 + p0c0)
c1

## Slide 50
Carry for the first two stages
c1 = g0 + p0 c0
c2 = g1 + p1g0 + p1p0c0
= g1 + p1 (g0 + p0c0)
= g1 + p1 c1
c1

## Slide 51
x
1
y
1
g
1
p
1
s
1
x
0
y
0
s
0
c
2
x
0
y
0
c
0
c
1
g
0
p
0
The first two stages of a carry-lookahead adder
[ Figure 3.15 from the textbook ]

## Slide 52
x
1
y
1
g
1
p
1
s
1
x
0
y
0
s
0
c
2
x
0
y
0
c
0
c
1
g
0
p
0
It takes 3 gate delays to generate c1
c1 = g0 + p0 c0

## Slide 53
x
1
y
1
g
1
p
1
s
1
x
0
y
0
s
0
c
2
x
0
y
0
c
0
c
1
g
0
p
0
It takes 3 gate delays to generate c2
c2 = g1 + p1g0 + p1p0c0

## Slide 54
x
1
y
1
g
1
p
1
s
1
x
0
y
0
s
0
x
0
y
0
c
0
c
1
g
0
p
0
The first two stages of a carry-lookahead adder
2
c

## Slide 55
x
1
y
1
g
1
p
1
s
1
x
0
y
0
s
0
x
0
y
0
c
0
c
1
g
0
p
0
It takes 4 gate delays to generate s1
2
c

## Slide 56
It takes 4 gate delays to generate s2
x
1
y
1
g
1
p
1
s
1
x
0
y
0
s
0
c
2
x
0
y
0
c
0
c
1
g
0
p
0
s
2

## Slide 57: N-bit Carry-Lookahead Adder
It takes 3 gate delays to generate all carry signals
It takes 1 more gate delay to generate all sum bits
Thus, the total delay through an n-bit carry-lookahead adder is only 4 gate delays!

## Slide 58
Expanding the Carry Expression
c1 = g0 + p0 c0
c2 = g1 + p1g0 + p1p0c0
ci+1 = gi + pi ci
c3 = g2 + p2g1 + p2p1g0 + p2p1p0c0
c8 = g7 + p7g6 + p7p6g5 + p7p6p5g4
+ p7p6p5p4g3 + p7p6p5p4p3g2
+ p7p6p5p4p3p2g1+ p7p6p5p4p3p2p1g0
+ p7p6p5p4p3p2p1p0c0
. . .

## Slide 59
Expanding the Carry Expression
c1 = g0 + p0 c0
c2 = g1 + p1g0 + p1p0c0
ci+1 = gi + pi ci
c3 = g2 + p2g1 + p2p1g0 + p2p1p0c0
c8 = g7 + p7g6 + p7p6g5 + p7p6p5g4
+ p7p6p5p4g3 + p7p6p5p4p3g2
+ p7p6p5p4p3p2g1+ p7p6p5p4p3p2p1g0
+ p7p6p5p4p3p2p1p0c0
. . .
Even this takes
only 3 gate delays

## Slide 60: N-bit Carry-Lookahead Adder
The complexity of an n-bit carry-lookahead adder increases rapidly as n becomes larger.
The preceding delay analysis assumes that gates with any number of inputs can be used. But, the number of gate inputs, referred to as the fan-in of the gate, has to be limited in practice (see Appendix B). Therefore the reality of fan-in constraints must be taken into account

## Slide 61
Block
x
31
24
–
c
32
c
24
y
31
24
–
s
31
24
–
x
15
8
–
c
16
y
15
8
–
s
15
8
–
c
8
x
7
0
–
y
7
0
–
s
7
0
–
c
0
3
Block
1
Block
0
A hierarchical carry-lookahead adder with
ripple-carry between blocks
x
23
16
–
y
23
16
–
s
23
16
–
Block
2

## Slide 62
Block
x
31
24
–
c
32
c
24
y
31
24
–
s
31
24
–
x
15
8
–
c
16
y
15
8
–
s
15
8
–
c
8
x
7
0
–
y
7
0
–
s
7
0
–
c
0
3
Block
1
Block
0
A hierarchical carry-lookahead adder with
ripple-carry between blocks
x
23
16
–
y
23
16
–
s
23
16
–
Block
2

## Slide 63
x
31
24
–
c
32
c
24
y
31
24
–
s
31
24
–
x
15
8
–
c
16
y
15
8
–
s
15
8
–
c
8
x
7
0
–
y
7
0
–
s
7
0
–
c
0
A hierarchical carry-lookahead adder with
ripple-carry between blocks
x
23
16
–
y
23
16
–
s
23
16
–

## Slide 64
Block
x
31
24
–
c
32
c
24
y
31
24
–
s
31
24
–
x
15
8
–
c
16
y
15
8
–
s
15
8
–
c
8
x
7
0
–
y
7
0
–
s
7
0
–
c
0
3
Block
1
Block
0
A hierarchical carry-lookahead adder with
ripple-carry between blocks
[ Figure 3.16 from the textbook ]

## Slide 65
Block
x
15
8
–
y
15
8
–
x
7
0
–
y
7
0
–
3
Block
1
Block
0
Second-level lookahead
c
0
s
7
0
–
P
0
G
0
P
1
G
1
P
3
G
3
s
15
8
–
s
31
24
–
c
8
c
16
c
32
x
31
24
–
y
31
24
–
c
24
[ Figure 3.17 from the textbook ]
A hierarchical carry-lookahead adder

## Slide 66
Block
x
15
8
–
y
15
8
–
x
7
0
–
y
7
0
–
3
Block
1
Block
0
Second-level lookahead
c
0
s
7
0
–
P
0
G
0
P
1
G
1
P
3
G
3
s
15
8
–
s
31
24
–
c
8
c
16
c
32
x
31
24
–
y
31
24
–
c
24
A hierarchical carry-lookahead adder
c
32

## Slide 67
Block
x
15
8
–
y
15
8
–
x
7
0
–
y
7
0
–
3
Block
1
Block
0
Second-level lookahead
c
0
s
7
0
–
P
0
G
0
P
1
G
1
P
3
G
3
s
15
8
–
s
31
24
–
c
8
c
16
c
32
x
31
24
–
y
31
24
–
c
24
A hierarchical carry-lookahead adder
c
32

## Slide 68
Block
x
15
8
–
y
15
8
–
x
7
0
–
y
7
0
–
3
Block
1
Block
0
Second-level lookahead
c
0
s
7
0
–
P
0
G
0
P
1
G
1
P
3
G
3
s
15
8
–
s
31
24
–
c
8
c
16
c
32
x
31
24
–
y
31
24
–
c
24
A hierarchical carry-lookahead adder
?
?
?
c
32

## Slide 69
The Hierarchical Carry Expression
c8 = g7 + p7g6 + p7p6g5 + p7p6p5g4
+ p7p6p5p4g3 + p7p6p5p4p3g2
+ p7p6p5p4p3p2g1+ p7p6p5p4p3p2p1g0
+ p7p6p5p4p3p2p1p0c0

## Slide 70
The Hierarchical Carry Expression
c8 = g7 + p7g6 + p7p6g5 + p7p6p5g4
+ p7p6p5p4g3 + p7p6p5p4p3g2
+ p7p6p5p4p3p2g1+ p7p6p5p4p3p2p1g0
+ p7p6p5p4p3p2p1p0c0

## Slide 71
The Hierarchical Carry Expression
c8 = g7 + p7g6 + p7p6g5 + p7p6p5g4
+ p7p6p5p4g3 + p7p6p5p4p3g2
+ p7p6p5p4p3p2g1+ p7p6p5p4p3p2p1g0
+ p7p6p5p4p3p2p1p0c0
G0
P0

## Slide 72
The Hierarchical Carry Expression
c8 = g7 + p7g6 + p7p6g5 + p7p6p5g4
+ p7p6p5p4g3 + p7p6p5p4p3g2
+ p7p6p5p4p3p2g1+ p7p6p5p4p3p2p1g0
+ p7p6p5p4p3p2p1p0c0
G0
P0
c8 = G0 + P0 c0

## Slide 73
The Hierarchical Carry Expression
c8 = G0 + P0 c0
c16 = G1 + P1 c8
= G1 + P1 G0 + P1 P0 c0
c24 = G2 + P2 G1 + P2 P1 G0 + P2 P1 P0 c0
c32 = G3 + P3 G2 + P3 P2 G1 + P3 P2 P1 G0+ P3 P2 P1 P0 c0

## Slide 74
Block
x
15
8
–
y
15
8
–
x
7
0
–
y
7
0
–
3
Block
1
Block
0
Second-level lookahead
c
0
s
7
0
–
P
0
G
0
P
1
G
1
P
3
G
3
s
15
8
–
s
31
24
–
c
8
c
16
c
32
x
31
24
–
y
31
24
–
c
24
[ Figure 3.17 from the textbook ]
A hierarchical carry-lookahead adder

## Slide 75
Block
x
15
8
–
y
15
8
–
x
7
0
–
y
7
0
–
3
Block
1
Block
0
Second-level lookahead
c
0
s
7
0
–
P
0
G
0
P
1
G
1
P
3
G
3
s
15
8
–
s
31
24
–
c
8
c
16
c
32
x
31
24
–
y
31
24
–
c
24
[ Figure 3.17 from the textbook ]
A hierarchical carry-lookahead adder
c8 = G0 + P0 c0
c16 = G1 + P1 G0 + P1 P0 c0
c32 =G3+P3G2+P3P2G1 +P3 P2 P1 G0+P3 P2 P1 P0 c0

## Slide 76: Hierarchical CLA Adder Carry Logic
C8 – 5 gate delays C16 – 5 gate delays C24 – 5 Gate delays C32 – 5 Gate delays

## Slide 77: Hierarchical CLA Critical Path
C9 – 7 gate delays C17 – 7 gate delays C25 – 7 Gate delays

## Slide 78: Total Gate Delay Through a Hierarchical Carry-Lookahead Adder
Is 8 gates
  3 to generate all Gj and Pj
  +2 to generate c8, c16, c24, and c32
  +2 to generate internal carries in the blocks
  +1 to generate the sum bits (one extra XOR)

## Slide 79: END Slide